## Slide 1
AXION
ARMv9 • SERVER CPU
COMPUTER ARCHITECTURE • TECHNICAL CASE STUDY
Google Axion
ARM-based CPU Architecture
How custom server silicon, Arm Neoverse cores and infrastructure offloads support efficient cloud and AI workloads
Aditya Ramane 16010125205
Atharva Rane 16010125205
Yashwardhan Rathod 16010125207
Architecture analysis • performance claims • limitations • references
OCTOBER 2026

## Slide 2
01 / MOTIVATION
Why does cloud infrastructure need a better CPU?
AI infrastructure is not only accelerators: CPUs handle orchestration, data movement, services and many inference workloads.
CPU BOTTLENECKS
Host-side preprocessing, request handling, databases and orchestration still consume substantial compute.
POWER & TCO
At hyperscale, small improvements in performance per watt can compound across thousands of servers.
WORKLOAD DIVERSITY
Web services, caches, analytics, storage and CPU-based inference need balanced general-purpose compute.
DESIGN RESPONSE
Axion combines Arm Neoverse CPU cores with Google’s custom silicon and Titanium infrastructure offloads.
COA lens: evaluate the ISA, core microarchitecture, memory hierarchy, I/O and system-level efficiency—not clock speed alone.
GOOGLE AXION | COMPUTER ORGANIZATION & ARCHITECTURE
02

## Slide 3
02 / ARCHITECTURE OVERVIEW
Axion is a system, not just an instruction set
Google designs the processor platform around Arm CPU IP and its data-centre environment.
APPLICATIONS
APIs • databases • analytics • media • CPU-side AI/ML
SOFTWARE STACK
Linux / Arm64 • runtimes • libraries • containers
ARM INSTRUCTION SET
AArch64 / Armv9 family; software-visible instruction contract
CPU MICROARCHITECTURE
Neoverse V2 in C4A; Neoverse N3 in N4A
GOOGLE AXION PLATFORM
Custom processor integration + memory / I/O / platform design
KEY DISTINCTION
Arm defines the ISA and core designs. Google integrates Axion for its cloud platform. Titanium offloads selected infrastructure tasks.
Do not describe Axion as a new proprietary ISA: it is an Arm-based CPU platform.
GOOGLE AXION | COMPUTER ORGANIZATION & ARCHITECTURE
03
ISA VS MICROARCHITECTURE
Arm defines the software-visible instruction set; Neoverse cores implement it. Arm64 compatibility matters for binaries, libraries and native dependencies.

## Slide 4
03 / DATA PATH
From request to useful work
CPU performance depends on feeding the cores and moving data through memory, storage and networking.
APPLICATION
instructions
CPU CORE
execute
DDR5 MEMORY
working set
TITANIUM / I/O
network + storage
MEMORY HIERARCHY
Registers → L1/L2 caches → DRAM. Cache hits reduce access latency; misses can stall dependent work.
SYSTEM-LEVEL DATA MOVEMENT
Network and storage traffic also consume resources. Offloading selected tasks can preserve CPU cycles for applications.
Important limit: Google does not publish a complete public Axion cache / pipeline block diagram in the sources used here; do not invent cache sizes or core counts.
GOOGLE AXION | COMPUTER ORGANIZATION & ARCHITECTURE
05
TITANIUM PLATFORM OFFLOAD
Selected networking, storage and infrastructure operations can be offloaded, preserving more host-CPU capacity for customer workloads. Benefits depend on workload and instance configuration.

## Slide 5
04/ EVALUATION
Performance claims: read the baseline carefully
Vendor-published headline comparisons are useful context, but they are not independent universal benchmark results.
UP TO 50%
performance vs comparable current-generation x86 instances (launch claim)
UP TO 60%
better energy efficiency vs comparable current-generation x86 instances (launch claim)
UP TO 30%
performance vs fastest general-purpose Arm-based cloud instances available at announcement
FAIR COMPARISON
Match workload, concurrency, memory, compiler, instance generation, power boundary and cost. Separate price-performance from raw throughput.
Google’s later C4A messaging reports different metrics for specific workloads (e.g., MySQL / Redis). Do not mix them into a single chart without matching baselines.
GOOGLE AXION | COMPUTER ORGANIZATION & ARCHITECTURE
07

## Slide 6
05 / WORKLOAD MAPPING
Where Axion fits—and why
The best candidate is a workload that is Arm-compatible and benefits from balanced CPU throughput, memory and I/O.
WEB / API SERVERS
Request handling, TLS, routing and application logic
DATABASES & CACHES
Query execution, transaction processing and in-memory access
ANALYTICS
Data preparation, query engines and batch processing
MEDIA / STREAMING
Transcoding pipelines and service-side processing
CPU-BASED AI INFERENCE
Selected small / medium models, preprocessing and serving
CONTAINERS / MICROSERVICES
Scale-out services and Kubernetes workloads
Not a TPU/GPU replacement: Axion runs general-purpose CPU work and can complement accelerators in an AI system.
GOOGLE AXION | COMPUTER ORGANIZATION & ARCHITECTURE
08

## Slide 7
06/ GOOGLE CLOUD DEPLOYMENT
C4A vs N4A: two Axion-backed VM families
Official Google Cloud documentation identifies different Neoverse cores and workload positioning.
FAMILY
CPU CORE
POSITIONING
SELECTED DETAILS
C4A
Arm Neoverse V2
Performance-oriented general purpose
Up to 72 vCPUs, 576 GB DDR5; Titanium SSD options on supported configurations
N4A
Arm Neoverse N3
Efficient scale-out / flexible general purpose
Up to 64 vCPUs, 512 GB DDR5; standard networking up to 50 Gbps
Specifications change over time; verify region, machine type, storage and networking limits before deployment.
Note: Google Cloud documents C4A and N4A as Arm-based Axion VM families; vCPU is one thread per core for these Arm platforms.
GOOGLE AXION | COMPUTER ORGANIZATION & ARCHITECTURE
09

## Slide 8
07 / CRITICAL ANALYSIS
Limitations, risks and open questions
A strong COA case study separates measured facts from marketing claims and identifies what public documentation does not reveal.
LIMITED MICROARCHITECTURE DISCLOSURE
Public materials do not provide a full core pipeline, cache hierarchy and branch-prediction specification.
SOFTWARE PORTABILITY
Arm64 images, native libraries, proprietary agents and build tooling must be validated.
BENCHMARK DEPENDENCE
Performance varies with instruction mix, working set, thread count, compiler and I/O intensity.
ACCELERATOR BOUNDARIES
CPU inference is useful for some models; large training and highly parallel tensor work may favour TPUs/GPUs.
Critical judgement: Axion’s strongest argument is system-level performance per watt—not a claim that Arm is always faster than x86.
GOOGLE AXION | COMPUTER ORGANIZATION & ARCHITECTURE
10

## Slide 9
8/ CONCLUSION
What should a COA student take away?
Axion illustrates how ISA, microarchitecture, memory/I/O and platform engineering combine in a modern server.
01
ISA & CORES
Arm architecture provides the software contract; Neoverse cores execute the instructions.
02
SYSTEM CO-DESIGN
Titanium shifts selected networking, storage and platform work away from host CPU cores.
03
MEASURED EFFICIENCY
Vendor claims must be interpreted against the stated workload and comparison baseline.
04
AI INFRASTRUCTURE ROLE
CPUs remain essential for orchestration, data systems and selected inference workloads alongside accelerators.
Final insight: evaluate the whole computing system, not only the CPU brand or instruction set.
GOOGLE AXION | COMPUTER ORGANIZATION & ARCHITECTURE
11

## Slide 10
REFERENCES
References
Official technical sources; formatted in IEEE, APA and ACM-like styles to mirror the reference presentation.
IEEE STYLE
[1] A. Vahdat, “Introducing Google’s new Arm-based CPU: Google Axion Processors,” Google Cloud Blog, Apr. 9, 2024. [Online]. Available: https://cloud.google.com/blog/products/compute/introducing-googles-new-arm-based-cpu
IEEE STYLE
[2] Google Cloud, “General-purpose machine family for Compute Engine: C4A and N4A,” Google Cloud Documentation. [Online]. Available: https://docs.cloud.google.com/compute/docs/general-purpose-machines
APA STYLE
Google Cloud. (2024, April 9). Introducing Google’s new Arm-based CPU: Google Axion Processors. Google Cloud Blog. https://cloud.google.com/blog/products/compute/introducing-googles-new-arm-based-cpu
ACM-STYLE
Google Cloud. 2024. Introducing Google’s new Arm-based CPU: Google Axion Processors. Google Cloud Blog (April 9, 2024). https://cloud.google.com/blog/products/compute/introducing-googles-new-arm-based-cpu
SUPPLEMENTARY
Google Cloud. (n.d.). Arm VMs on Compute Engine. https://docs.cloud.google.com/compute/docs/instances/arm-on-compute
SUPPLEMENTARY
Arm. (2025, April 9). Unpacking Axion: Google Cloud’s custom Arm-based processor built for the AI age. https://newsroom.arm.com/blog/google-cloud-axion-arm-ai-performance
Accessed 19 October 2026. Performance figures are attributed to the source that reports them.
GOOGLE AXION | COMPUTER ORGANIZATION & ARCHITECTURE
12